## Slide 1: Background traffic plugin

## Slide 2: What is it
Background Traffic Plug-in is a tool which allows tester to add traffic verification to any test case with minimal effort. It will handle traffic generators(apply/cleanup configuration) in background, according to XML configuration files provided by user. Traffic evaluation can be done in background or foreground depending on the type of evaluation and test case purpose. Plug-in is based on TG Library, therefore it inherits all limitations of TG library.

## Slide 3: Configuration set up
You need to specify a main configuration file with a VM argument
-Dbat=/home/git/jcat_ebs_tg_config_plugin/src/main/resources/examples/bat.xml
You can also specify a VM argument to enable/disable the validation of the configuration files content. If the argument is omitted it is considered to be true
-Dbat.validation=true
All config files support freemarker injection. Variable can be specified by VM argument
-Dbat.variables=/home/git/jcat_ebs_tg_config_plugin/src/main/resources/examples/vars

## Slide 4: bat.xml
bat.xml is the mail file needed to set up background traffic plugin settings
<?xml version="1.0" encoding="UTF-8"?> <bat xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xsi:schemaLocation="http://www.ericsson.com/commonlibrary/bat/cfg https://arm.rnd.ki.sw.ericsson.se/artifactory/proj-switching-jcat-seki-dev/com/ericsson/commonlibrary/bat-description/xsd/1.0.38/bat/BAT.xsd" xmlns="http://www.ericsson.com/commonlibrary/bat/cfg"> <traffic_generators>src/site/resources/examples/Ixia.xml</traffic_generators> <configuration>src/site/resources/examples/BackgroundTraffic.xml</configuration> <traffic_rules>src/site/resources/examples/TrafficRules.xml</traffic_rules> <testcase_rules>src/site/resources/examples/TestcaseRules.xml</testcase_rules> </bat>

## Slide 5: Entry points
bat.xml is the mail file needed to set up background traffic plugin settings
<?xml version="1.0" encoding="UTF-8"?> <bat xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xsi:schemaLocation="http://www.ericsson.com/commonlibrary/bat/cfg https://arm.rnd.ki.sw.ericsson.se/artifactory/proj-switching-jcat-seki-dev/com/ericsson/commonlibrary/bat-description/xsd/1.0.38/bat/BAT.xsd" xmlns="http://www.ericsson.com/commonlibrary/bat/cfg"> <traffic_generators>/home/xivasyn/git/jcat_ebs_tg_config_plugin/src/site/resources/examples/Ixia.xml</traffic_generators> <configuration>/home/xivasyn/git/jcat_ebs_tg_config_plugin/src/site/resources/examples/BackgroundTraffic.xml</configuration> <traffic_rules>/home/xivasyn/git/jcat_ebs_tg_config_plugin/src/site/resources/examples/TrafficRules.xml</traffic_rules> <testcase_rules>/home/xivasyn/git/jcat_ebs_tg_config_plugin/src/site/resources/examples/TestcaseRules.xml</testcase_rules> </bat>

## Slide 6: How to create TG instance
Instead of using low level API, se.ericsson.jcat.ebs.traffic.TrafficGenerator wrapper is used.
TrafficGenerator tg = TrafficGenerator.getInstance();
The code above takes care about getting appropriate TG implementation, downloading the latest TCL API and setting up the environment.

## Slide 7: Port allocation
The first step towards configuring traffic is to allocate the traffic generator ports that should be used.
In case if ebs-properties are used, no additional information is needed.
TrafficGeneratorInterface tgInterface = TrafficGeneratorProperties.getTrafficGeneratorInterface(bladeInterface); TrafficGeneratorPort tgPort = tg.allocatePort(tgInterface);
The first time a port is allocated on a traffic generator chassis a connection will be established. This connection will be re-used during allocation of any subsequent port allocations on the same traffic generator. Port allocation may fail because of network access limitations, incorrect information regarding TCL API location or version, or if the port is already occupied by another user.
The TG has to be disconnected safely even if test case failed or crashed with exception.
tg.disconnect();

## Slide 8: Stream configuration
Stream configuration
Traffic generator streams are created per port and can be modified individually.
TrafficGeneratorStream stream = tg.createStream(tgPort, frameSize, fps);
Protocol objects are used to configure the header fields of packets in a stream.
Ipv4 ip = new Ipv4(); ip.setDestinationAddress(destinationIp); ip.setSourceAddress(sourceIp); stream.addProtocol(ip);
Traffic generator defaults will be used for all values that are not explicitly configured. If destination MAC address has not been defined but IPv4 has been added to the configuration ARP will be used to resolve the destination.
To actually configure the stream on the traffic generator(s) the configuration must be committed. This should only be done once before starting traffic the first time, or after re-configuration, to save time during test execution.
tg.commitConfiguration();

## Slide 9: Stream configuration
Stream configuration
Traffic generator streams are created per port and can be modified individually.
TrafficGeneratorStream stream = tg.createStream(tgPort, frameSize, fps);
Protocol objects are used to configure the header fields of packets in a stream.
Ipv4 ip = new Ipv4(); ip.setDestinationAddress(destinationIp); ip.setSourceAddress(sourceIp); stream.addProtocol(ip);
Traffic generator defaults will be used for all values that are not explicitly configured. If destination MAC address has not been defined but IPv4 has been added to the configuration ARP will be used to resolve the destination.
To actually configure the stream on the traffic generator(s) the configuration must be committed. This should only be done once before starting traffic the first time, or after re-configuration, to save time during test execution.
tg.commitConfiguration();

## Slide 10: Running traffic
Traffic is started on all allocated traffic generator ports regardless of the chassis in which they are located.
tg.startTraffic();
Traffic is stopped on all allocated traffic generator ports regardless of the chassis in which they are located.
tg.stopTraffic();

## Slide 11: Statistic counters
The traffic generator library offers a generic set of counters that can be used to evaluate traffic. To ensure a consistent behavior between supported traffic generators it is mandatory to subscribe to the wanted counters before starting traffic.
Counter subscription
Both port and stream level statistics are supported by the traffic generator library.
Any port counters that are subscribed to will be enabled for all ports in the configuration.
tg.subscribeCounter(StatisticCounter.FRAMES_TX); tg.subscribeCounter(StatisticCounter.FRAMES_RX);
Any stream counters that are subscribed to will be enabled for all streams in the configuration.
tg.subscribeStreamCounter(StatisticStreamCounter.STREAM_PACKETS_TEST_RX); tg.subscribeStreamCounter(StatisticStreamCounter.STREAM_PACKETS_TEST_TX);
To actually subscribe to any counter on the traffic generator(s) the configuration must be committed. This should be done together with the stream configuration to save time during test execution.
tg.commitConfiguration();

## Slide 12: Statistic collection
Port statistics are retrieved for all ports in a sequential manner. In order to get consistent values it is recommended to only read counter values after traffic has already stopped, unless counters measuring throughput are used.
Map<TrafficGeneratorPort, Map<StatisticCounter, Double>> portStatistics = tg.getPortStatistics(); Double txPortCounter = portStatistics.get(tgPort).get(StatisticCounter.FRAMES_TX);
Stream statistics are retrieved for all streams in a sequential manner. In order to get consistent values it is recommended to only read counter values after traffic has already stopped, unless counters measuring throughput are used.
Map<TrafficGeneratorStream, Map<StatisticStreamCounter, Double>> streamStatistics = tg.getStreamStatistics(); Double txStreamCounter = streamStatistics.get(stream).get(StatisticStreamCounter.STREAM_PACKETS_TEST_RX);
Counter values can only be retrieved for counters that have been already subscribed to.
Clear counter values
To get ensure that only counter values applicable to the current test are used it is recommended to clear the counter values on the traffic generator(s) between measurements.
tg.clearStatistics();

## Slide 13: TG properties
Ebs-properties have a special element to provide setting for TG and Lab manager:
<interface > <name>eth0</name> <protocol>ssh</protocol> <connection> <labmanager> <port>5</port> <xi:include href="src/test/resources/LabmanagerAccess.xml"> <xi:fallback> <xi:include href="LabmanagerAccess.xml" /> </xi:fallback> </xi:include> <xi:include href="src/test/resources/TrafficGenerator.xml"> <xi:fallback> <xi:include href="TrafficGenerator.xml" /> </xi:fallback> </xi:include> </labmanager> </connection> </interface>

## Slide 14: TG properties
You can specify TG settings in XML
<?xml version="1.0" encoding="UTF-8"?> <tg xmlns="http://www.ericsson.se/jcat/ebs/properties/trafficgenerator" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xmlns:xi="http://www.w3.org/2001/XInclude" xsi:schemaLocation="http://www.ericsson.se/jcat/ebs/properties/trafficgenerator ../xsd/TrafficGenerator.xsd "> <xi:include href="TrafficGeneratorAccess.xml" /> <xi:include href="TrafficGeneratorData.xml" /> <chassis>0</chassis> <card>0</card> <port>0</port> <speed>100M</speed> </tg>
<?xml version="1.0" encoding="UTF-8"?> <tg_data xmlns="http://www.ericsson.se/jcat/ebs/properties/trafficgeneratordata" xmlns:def= "http://www.ericsson.se/jcat/ebs/properties/definitions" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xsi:schemaLocation="http://www.ericsson.se/jcat/ebs/properties/trafficgeneratordata ../xsd/TrafficGeneratorData.xsd" > <api_path>ixia/5.60/ixTclHal.tcl</api_path> <version>5.60</version> <lab_server> <def:ipv4>192.168.0.1</def:ipv4> </lab_server> <tg_session>session_name</tg_session> <port_reset_time unit="SECONDS">1</port_reset_time> </tg_data>