## Slide 1: Traffic generator library

## Slide 2: What is a traffic generator
Traffic Generator is a tool that allows to evaluate performance of DUT (Device Under Test) or SUT (System Under Test). Tool can generate and send RAW packets over specific ports. It also collects latency and jitter values, tx/rx rates, counts lost packets and detects Out-of-Order (OOO) packets

## Slide 3: TG library
Within Ericsson there are a lot of different traffic generators used for generating traffic during testing.
TG types:
Software(trex)
Hardware(Agilent, ixia, spirent)
The thought behind TG is to provide a common interface with different methods for communication with a traffic generator, which means that regardless of the traffic generator type and brand, the test cases will always use the same methods. Meaning, no modification of the test cases will be needed, but several different traffic generators can be used by the same test case.

## Slide 4: TG library overview
Spirent TG implementation
Spirent TCL API
Ixia TCL API
Test case
TG library common API
Ebs-extensions wrappers
Test level wrappers
Trex API
TCL blend
Agilent TG implementation
Ixia TG implementation
Agilent TCL API

## Slide 5: API software
TCL API files
All traffic generators use their own TCL API for communication with the hardware. The API files are acquired by ITTE from the vendor and distributed among users according to their licenses. In the general case it is recommended to use an API of the same version as the software on the traffic generator itself. The only exception is when the traffic generator officially has backward compatibility with older versions.
TRex software
TRex is a software based free open-source traffic generator, it's still on the way to be improved or evolved. To utilize all the feature provided by traffic-generator, please always download and install the latest TRex software version. And it's more recommended to install eTRex instead of official one, eTRex is the value-added TRex for basic and Ericsson specific features

## Slide 6: How to create TG instance
Instead of using low level API, se.ericsson.jcat.ebs.traffic.TrafficGenerator wrapper is used.
TrafficGenerator tg = TrafficGenerator.getInstance();
The code above takes care about getting appropriate TG implementation, downloading the latest TCL API and setting up the environment.

## Slide 7: Port allocation
The first step towards configuring traffic is to allocate the traffic generator ports that should be used.
In case if ebs-properties are used, no additional information is needed.
TrafficGeneratorInterface tgInterface = TrafficGeneratorProperties.getTrafficGeneratorInterface(bladeInterface); TrafficGeneratorPort tgPort = tg.allocatePort(tgInterface);
The first time a port is allocated on a traffic generator chassis a connection will be established. This connection will be re-used during allocation of any subsequent port allocations on the same traffic generator. Port allocation may fail because of network access limitations, incorrect information regarding TCL API location or version, or if the port is already occupied by another user.
The TG has to be disconnected safely even if test case failed or crashed with exception.
tg.disconnect();

## Slide 8: Stream configuration
Stream configuration
Traffic generator streams are created per port and can be modified individually.
TrafficGeneratorStream stream = tg.createStream(tgPort, frameSize, fps);
Protocol objects are used to configure the header fields of packets in a stream.
Ipv4 ip = new Ipv4(); ip.setDestinationAddress(destinationIp); ip.setSourceAddress(sourceIp); stream.addProtocol(ip);
Traffic generator defaults will be used for all values that are not explicitly configured. If destination MAC address has not been defined but IPv4 has been added to the configuration ARP will be used to resolve the destination.
To actually configure the stream on the traffic generator(s) the configuration must be committed. This should only be done once before starting traffic the first time, or after re-configuration, to save time during test execution.
tg.commitConfiguration();

## Slide 9: Stream configuration
Stream configuration
Traffic generator streams are created per port and can be modified individually.
TrafficGeneratorStream stream = tg.createStream(tgPort, frameSize, fps);
Protocol objects are used to configure the header fields of packets in a stream.
Ipv4 ip = new Ipv4(); ip.setDestinationAddress(destinationIp); ip.setSourceAddress(sourceIp); stream.addProtocol(ip);
Traffic generator defaults will be used for all values that are not explicitly configured. If destination MAC address has not been defined but IPv4 has been added to the configuration ARP will be used to resolve the destination.
To actually configure the stream on the traffic generator(s) the configuration must be committed. This should only be done once before starting traffic the first time, or after re-configuration, to save time during test execution.
tg.commitConfiguration();

## Slide 10: Running traffic
Traffic is started on all allocated traffic generator ports regardless of the chassis in which they are located.
tg.startTraffic();
Traffic is stopped on all allocated traffic generator ports regardless of the chassis in which they are located.
tg.stopTraffic();

## Slide 11: Statistic counters
The traffic generator library offers a generic set of counters that can be used to evaluate traffic. To ensure a consistent behavior between supported traffic generators it is mandatory to subscribe to the wanted counters before starting traffic.
Counter subscription
Both port and stream level statistics are supported by the traffic generator library.
Any port counters that are subscribed to will be enabled for all ports in the configuration.
tg.subscribeCounter(StatisticCounter.FRAMES_TX); tg.subscribeCounter(StatisticCounter.FRAMES_RX);
Any stream counters that are subscribed to will be enabled for all streams in the configuration.
tg.subscribeStreamCounter(StatisticStreamCounter.STREAM_PACKETS_TEST_RX); tg.subscribeStreamCounter(StatisticStreamCounter.STREAM_PACKETS_TEST_TX);
To actually subscribe to any counter on the traffic generator(s) the configuration must be committed. This should be done together with the stream configuration to save time during test execution.
tg.commitConfiguration();

## Slide 12: Statistic collection
Port statistics are retrieved for all ports in a sequential manner. In order to get consistent values it is recommended to only read counter values after traffic has already stopped, unless counters measuring throughput are used.
Map<TrafficGeneratorPort, Map<StatisticCounter, Double>> portStatistics = tg.getPortStatistics(); Double txPortCounter = portStatistics.get(tgPort).get(StatisticCounter.FRAMES_TX);
Stream statistics are retrieved for all streams in a sequential manner. In order to get consistent values it is recommended to only read counter values after traffic has already stopped, unless counters measuring throughput are used.
Map<TrafficGeneratorStream, Map<StatisticStreamCounter, Double>> streamStatistics = tg.getStreamStatistics(); Double txStreamCounter = streamStatistics.get(stream).get(StatisticStreamCounter.STREAM_PACKETS_TEST_RX);
Counter values can only be retrieved for counters that have been already subscribed to.
Clear counter values
To get ensure that only counter values applicable to the current test are used it is recommended to clear the counter values on the traffic generator(s) between measurements.
tg.clearStatistics();

## Slide 13: TG properties
Ebs-properties have a special element to provide setting for TG and Lab manager:
<interface > <name>eth0</name> <protocol>ssh</protocol> <connection> <labmanager> <port>5</port> <xi:include href="src/test/resources/LabmanagerAccess.xml"> <xi:fallback> <xi:include href="LabmanagerAccess.xml" /> </xi:fallback> </xi:include> <xi:include href="src/test/resources/TrafficGenerator.xml"> <xi:fallback> <xi:include href="TrafficGenerator.xml" /> </xi:fallback> </xi:include> </labmanager> </connection> </interface>

## Slide 14: TG properties
You can specify TG settings in XML
<tg xsi:schemaLocation="http://www.ericsson.se/jcat/ebs/properties/trafficgenerator ../xsd/TrafficGenerator.xsd "> <xi:include href="TrafficGeneratorAccess.xml" /> <xi:include href="TrafficGeneratorData.xml" /> <chassis>0</chassis> <card>0</card> <port>0</port> <speed>100M</speed> </tg>
<tg_data xmlns="http://www.ericsson.se/jcat/ebs/properties/trafficgeneratordata" xsi:schemaLocation="http://www.ericsson.se/jcat/ebs/properties/trafficgeneratordata ../xsd/TrafficGeneratorData.xsd" > <api_path>ixia/5.60/ixTclHal.tcl</api_path> <version>5.60</version> <lab_server> <def:ipv4>192.168.0.1</def:ipv4> </lab_server> <tg_session>session_name</tg_session> <port_reset_time unit="SECONDS">1</port_reset_time> </tg_data>
<access xmlns="http://www.ericsson.se/jcat/ebs/properties/access" xsi:schemaLocation="http://www.ericsson.se/jcat/ebs/properties/access ../xsd/Access.xsd "> <def:address> <def:ipv4>10.255.0.6</def:ipv4> <def:port>22</def:port> </def:address> <def:user> <def:name>ixia</def:name> <def:password>ixia123</def:password> </def:user> <vendor>Ixia</vendor> </access>